## Slide 1
IoT comprises things that have unique identities and are connected to internet. By 2020 there will be a total of 50 billion devices /things connected to internet. IoT is not limited to just connecting things to the internet but also allow things to communicate and exchange data.
Definition:
A dynamic global n/w infrastructure with self configuring capabilities based on standard and interoperable communication protocols where physical and virtual ―things‖ have identities, physical attributes and virtual personalities and use intelligent interfaces, and are seamlessly integrated into information n/w, often communicate data associated with users and their environments.
INTRODUCTION OF IOT

## Slide 2
Characteristics:
Dynamic & Self Adapting: IoT devices and systems may have the capability to
dynamically adapt with the changing contexts and take actions based on their
operating conditions, user’s context or sensed environment.
Eg: The surveillance system is adapting itself based on context and changing
conditions.
2) Self Configuring: Allowing a large number of devices to work together to
provide certain functionality.
3) Inter Operable Communication Protocols: Support a number of interoperable
communication protocols and can communicate with other devices and also with
infrastructure.
4) Unique Identity: Each IoT device has a unique identity and a unique identifier
(IP address).
5) Integrated into Information Network: That allow them to communicate and
exchange data with other devices and systems.

## Slide 3
Applications of IoT:
1) Home
2) Cities
3) Environment
4) Energy
5) Retail
6) Logistics
7) Agriculture
8) Industry
9) Health & Life Style

## Slide 6
Physical Design of IoT

## Slide 7
The things in IoT refers to IoT devices which have unique identities and perform remote sensing, actuating and monitoring capabilities.
IoT devices can exchange data with other connected devices applications. It collects data from other devices and process data either locally or remotely.
An IoT device may consist of several interfaces for communication to other devices both wired and wireless. These includes
(i) I/O interfaces for sensors,
(ii) Interfaces for internet connectivity
(iii) memory and storage interfaces and
(iv) audio/video interfaces.
1) Things in IoT:

## Slide 9
2) IoT Protocols:
Link Layer : Protocols determine how data is physically sent over the network’s physical layer or medium. Local network connect to which host is attached. Hosts on the same link exchange data packets over the link layer using link layer protocols. Link layer determines how packets are coded and signalled by the h/w device over the medium to which the host is attached.
Protocols:
 802.3-Ethernet: IEEE802.3 is collection of wired Ethernet standards for the link layer. Eg: 802.3 uses co-
axial cable; 802.3i uses copper twisted pair connection; 802.3j uses fiber optic connection; 802.3ae uses
Ethernet over fiber.
 802.11-WiFi: IEEE802.11 is a collection of wireless LAN(WLAN) communication standards including
extensive description of link layer. Eg: 802.11a operates in 5GHz band, 802.11b and 802.11g operates in
2.4GHz band, 802.11n operates in 2.4/5GHz band, 802.11ac operates in 5GHz band, 802.11ad operates in
60Ghzband.
 802.16 - WiMax: IEEE802.16 is a collection of wireless broadband standards including exclusive
description of link layer. WiMax provide data rates from 1.5 Mb/s to 1Gb/s.
 802.15.4-LR-WPAN: IEEE802.15.4 is a collection of standards for low rate wireless personal area
network(LR-WPAN). Basis for high level communication protocols such as ZigBee. Provides data rate
from 40kb/s to250kb/s.
 2G/3G/4G-Mobile Communication: Data rates from 9.6kb/s(2G) to up to100Mb/s(4G).

## Slide 10
b) Network/Internet Layer: Responsible for sending IP datagrams from source n/w to destination n/w. Performs the host addressing and packet routing. Datagrams contains source and destination address.
Protocols:
IPv4: Internet Protocol version4 is used to identify the devices on a n/w using a hierarchical addressing scheme. 32 bit address. Allows total of 2**32addresses.
IPv6: Internet Protocol version6 uses 128 bit address scheme and allows 2**128 addresses.
6LOWPAN:(IPv6overLowpowerWirelessPersonalAreaNetwork)operates in
2.4 GHz frequency range and data transfer 250 kb/s.

## Slide 11
c) Transport Layer: Provides end-to-end message transfer capability independent of the underlying n/w. Set up on connection with ACK as in TCP and without ACK as in UDP. Provides functions such as error control, segmentation, flow control and congestion control.
Protocols:
 TCP: Transmission Control Protocol used by web browsers(along with HTTP
and HTTPS), email(along with SMTP, FTP). Connection oriented and
stateless protocol. IP Protocol deals with sending packets, TCP ensures
reliable transmission of protocols in order. Avoids n/w congestion and
congestion collapse.
 UDP: User Datagram Protocol is connectionless protocol. Useful in time
sensitive applications, very small data units to exchange. Transaction oriented
and stateless protocol. Does not provide guaranteed delivery.

## Slide 12
d) Application Layer: Defines how the applications interface with lower layer protocols to send data over the n/w. Enables process-to-process communication using ports.
Protocols:
 HTTP: Hyper Text Transfer Protocol that forms foundation of WWW. Follow request- response
model Stateless protocol.
 CoAP: Constrained Application Protocol for machine-to-machine (M2M) applications with
constrained devices, constrained environment and constrained n/w. Uses client- server architecture.
 WebSocket: allows full duplex communication over a single socket connection.
 MQTT: Message Queue Telemetry Transport is light weight messaging protocol based on publish-
subscribe model. Uses client server architecture. Well suited for constrained environment.
 XMPP: Extensible Message and Presence Protocol for real time communication and streaming XML
data between network entities. Support client-server and server-server communication.
 DDS: Data Distribution Service is data centric middleware standards for device-to-device or
machine-to-machine communication. Uses publish-subscribe model.
 AMQP: Advanced Message Queuing Protocol is open application layer protocol for business
messaging. Supports both point-to-point and publish-subscribe model.

## Slide 13
LOGICAL DESIGN of IoT
Refers to an abstract represent of entities and processes without going into the low level specifies of implementation.
1) IoT Functional Blocks 2) IoT Communication Models 3) IoT Comm. APIs
1) IoT Functional Blocks: Provide the system the capabilities for identification, sensing, actuation, communication and management.

## Slide 14
Device: An IoT system comprises of devices that provide sensing, actuation, monitoring and control functions.
Communication: handles the communication for IoT system.
Services: for device monitoring, device control services, data publishing services and services for device discovery.
Management: Provides various functions to govern the IoT system.
Security: Secures IoT system and priority functions such as authentication, authorization, message and context integrity and data security.
Application: IoT application provide an interface that the users can use to control and monitor various aspects of IoT system.
2) IoT Communication Models:
1) Request-Response
2) Publish-Subscribe
3)Push-Pull
4) Exclusive Pair

## Slide 15
1) Request-Response Model:
In which the client sends request to the server and the server replies to requests. Is a stateless communication model and each request-response pair is independent of others.

## Slide 16
2) Publish-Subscribe Model:
Involves publishers, brokers and consumers. Publishers are source of data. Publishers send data to the topics which are managed by the broker. Publishers are not aware of the consumers. Consumers subscribe to the topics which are managed by the broker. When the broker receives data for a topic from the publisher, it sends the data to all the subscribed consumers.

## Slide 17
3) Push-Pull Model: In which data producers push data to queues and consumers pull data from the queues. Producers do not need to aware of the consumers. Queues help in decoupling the message between the producers and consumers.

## Slide 18
4) Exclusive Pair: It is bi-directional, fully duplex communication model that uses a persistent connection between the client and server. Once connection is set up it remains open until the client send a request to close the connection. Is a stateful communication model and server is aware of all the open connections.